## Slide 1: Lesson 2: Z-Wave Fundamentals
Notes: Need more info on:
Beam
Wake up CMD class

## Slide 2: Z-wave protocol purpose
Provides resilient network requiring little to no maintenance
Allows for a wide range of battery powered nodes
Provides backwards compatibility to any Z-wave device while offering newest features to the node supporting them
UL1023 certified for Household Burglar-Alarm
Notes: The routing protocol allows for stable frame delivery

## Slide 3: Z-Wave PHY/MAC
Public PHY/MAC specification ITU G.9959
  https://www.itu.int/rec/T-REC-G.9959-201501-I/en
Z-Wave Frequency Allocation ZAD12837-10
  https://zwavealliance.org/wp-content/uploads/2018/03/ZAD12837-10.pdf
Sub GHz, license free ISM bands, region/Country specific
Data rate \ region frequency & channel(s) | US / Canada / South America | EU / UAE / China / India | AU / NZ / Brazil | Japan / Taiwan / Korea / Singapore
9.6kbps FSK Modulation | 908 MHz Ch 1 | 868 MHz Ch 1 | 921 MHz Ch 1 | NA
40kpbs FSK Modulation | 908 MHz Ch 1 | 868 MHz Ch 1 | 921 MHz Ch 1 | NA
100kpbs GFSK Modulation | 916 MHZ Ch 2 | 869 MHz Ch 2 | 919 MHz Ch 2 | 919-926 MHz Ch 1 - 3
Notes: Z-wave is based on the UT
Benefits of Sub G: Longe range at lower frequency
Downside: different frequency allocation for different regions.

## Slide 4: Z-Wave PHY/MAC - ADDRESSING
Home ID, 32 bit network identifier
  Randomly generated in all unincluded nodes*
  Home ID will be the same as Controller Home ID upon inclusion to its network
Node ID, 8 bit node identifier
  0 at startup*
  Changed at inclusion into network
  Max nodes in a network 232
Frame Types
  Singlecast
  Multicast
  Broadcast
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Home ID (0) |  |  |  |  |  |  | 
Home ID (1) |  |  |  |  |  |  | 
Home ID (2) |  |  |  |  |  |  | 
Home ID (3) |  |  |  |  |  |  | 
Source Node ID |  |  |  |  |  |  | 
Routed | Ack | Low | Speed | Header Type |  |  | 
Wakeup |  |  | Reserved | Sequence Number |  |  | 
Length |  |  |  |  |  |  | 
Destination ID |  |  |  |  |  |  | 
Data byte 0-x |  |  |  |  |  |  | 
.. |  |  |  |  |  |  | 
.. |  |  |  |  |  |  | 
Checksum (0) |  |  |  |  |  |  | 
Checksum (1) |  |  |  |  |  |  | 
Singlecast
Dest = 02
Transfer Ack
Dest = 01

## Slide 5: Z-Wave routing algorithm components
Routing Table
  Routing table is built during inclusion
  Routing table is updated on demand
Cached Routes
  Last working route (LWR) are always cached and used first
  Application Programmable Priority Routes
    Application can push routes to the protocol
Dynamic route resolution
  Explorer Frames and Intelligent Flooding
Notes: The routing table is held by the controller
Routing table is built during inclusion through neighbor discovery.
Neighbor discovery can be invoked at any time to refresh the routing table hold by the controller
The Controller caches the the last working route LWR, and uses this by default
Simliarly the slave nodes relies on the response routes, i.e. Respond through the route a request was received through.
If a slave sends unsolicited reports, it relies on assigned return routes.
Explorer frames are used as a last resort if the destination cannot be reached. The network is flooded with, and if the destionation is reached, it acks the frame. The ack is used to updated the ”last working route” / response route.

## Slide 6: Z-Wave Routing
Routing
  Source Routing – 4 hops max.
  Singlecast with silent acknowledge
Routed Singlecast (1)
Routed Ack (4)
Ack (5)
Routed Singlecast (2)
Routed Ack (3)
3
4

## Slide 7: Dynamic route resolution
Explorer Frames
  Use:
    Broadcast flooding
    TTL
    Loop back prevention
  It is used to discover/rediscover routes
  Application command is included in the explorer frame
Explorer Frame Response
  Explorer response uses source routing
  Becomes the LWR when received
  Implements random back off to avoid collisions
Explorer frame
Search result frame

## Slide 8: Z-Wave Device Inclusion
Assign HomeID and NodeID
Range info: I can see 2, 4, and 5
Look for NodeID 2, 3, 4, and 5
Node Information Frame
Inclusion
  Home ID and Node ID are assigned
  New node is asked to look for neighbors
Secure Bootstrapping
  Exchange of keys
Device probing
  All CC information are extracted and configured if needed
NOP
ACK
6
2
5
4
New Node
1

## Slide 9: Removing nodes
Similar to add node
  Except that the assigned home and node IDs are all zero

## Slide 10: Remove / Replace failed
Replace failed
  Replace failed is only intended to replace failed nodes with an identical device.
  Node must be marked as ”failed” by the protocol
  Controller attempts to reach destination node 3 times
  If destination node cannot be reached, the controller enters inclusion mode, and assigns the home ID of the failed node to a new node.
Remove failed
  Node must be marked as ”failed” by the protocol
  Controller attempts to reach destination node 3 times
  If destination node cannot be reached, the destination node is removed from the controllers routing table with attempting verify that the home and node ID was deassigned from the node.
Notes: Remove failed
Allows for removing a failed/unresponsive node without deassigning the node ID from the unresponsive node.
Replace failed
Allows for reusing an already assigned node ID from a failed/unresponsive node. This allows the user to replace a failing node without having to reassign associations and return routes in a peer to peer scenario, or modify scenes in a controller centric setup.

## Slide 11: The Node Information Frame [NIF]
The business card of the Z-wave node
Announces protocol and Application level capabilities

## Slide 12: Node types
Mains powered
  Static controller
  Always on Slave [AOS]
Battery powered
  Reporting Sleeping Slave [RSS]
  Listening Sleeping Slave [LSS]
Legacy types (500 series and earlier)
  Portable Controller [PC]
  Reporting Portable Controller [RPC]

## Slide 13: Always On Slave [AOS] / Controllers
Always reachable
  Can receive and send commands at all times
The back-bone of the Z-wave mesh
  Is a repeater in the network
Notes: AOS nodes improves the routing properties of Z-wave by each node serving as repeater for the other nodes in the network.

## Slide 14: Listening Sleeping Slave [LSS]
Listens at a fixed interval
  250ms or 1000 ms
Battery Powered
Can be reached by all nodes with latency <= 1s
Will wake up on timer or on events
Cannot be used as repeater

## Slide 15: Reporting Sleeping Slave [RSS]
Battery Powered
Can not be reached by all nodes
Will wake up on timer or on events

## Slide 16: Assigning return routes
Slaves does not by default know how other slaves can be reached
Assign Return route
  Speed
    Based on speed supported by routing hops and destination node
  Routing hops required to reach the destination
  Power state; is the destination a LSS
  Multiple return routes can be assigned – up to 4
Notes: If not routes are assigned, the protocol will try single hop 40kbps
Assigning routes allows for:
Improved speed
Reaching FLIRS nodes
Using routing hops to reach the destination.
Everything based on the NIF of source, destination and intermediate routing hops.
Higher level functionality such as security can be routed through nodes not supporting these command classes.

## Slide 17: Associations
- What to send where

## Slide 18: What are associations?
The Association Command Class is used to manage associations to NodeID destinations.
Allow a controller to automate interactions between nodes
Notes: A NodeID destination may be a simple device or the Root Device of a Multi Channel device.

## Slide 19: What Really are associations?
Table of list
Each list has members that are subscribed to it
Each list has a specific function
Notes: That was a description but associations really are a table of lists
Each separate list has a different function defined by the manufacturer
Each list has a group of nodes that it will contact based on different events

## Slide 20: How do associations work?
1
4
3
2
Group No. | Group Name | Nodes in Group
1 | llifeline | 
2 | on/off | 
Group No. | Group Name | Nodes in Group
1 | llifeline | 
Group No. | Group Name | Nodes in Group
1 | llifeline | 
Set ID1 into lifeline group
Set ID1 into lifeline group
Set ID1 into lifeline group
Group No. | Group Name | Nodes in Group
1 | llifeline | 1
2 | on/off | 
Group No. | Group Name | Nodes in Group
1 | lifeline | 1
Group No. | Group Name | Nodes in Group
1 | lifeline | 1
Set ID4 and 3 into group 2
Group No. | Group Name | Nodes in Group
1 | lifeline | 1
2 | on/off | 3,4
Motion Triggered
Turn Siren On
Turn Alert Light On
Notes: The first group on any ZW+ device is the “Lifeline” group
The rest of the association groups are

## Slide 21: Wakeup Command Class

## Slide 22: Wakeup Command Class configuration
Controller must
  Query nodes for they wakeup intervals
    Minimum, maximum and default wakeup interval
  Set the wakeup interval and destination
Slave must
  … implement a Minimum Wake Up Interval in the range 0 ..4200 (i.e. between 0 second and 70 minutes).
Notes: The routing protocol allows for stable frame delivery

## Slide 23: Wakeup runtime communication
Slave sends wakeup notification at fixed interval
Upon wake up notification controllers
  Sends queued traffic
  Puts node back to sleep

## Slide 24: Thank you!
silabs.com
End of Lesson 2: Z-Wave Fundamentals